Projekt: Cache Controller für ARM Cortex M0 on a Xilinx Spartan 6

# Motivation
The performance of processors and microcontrollers is heavily depending on the memory performance, especially how fast we can load instructions ans data from the memory. The figure shows the current architecture of the system. It has no Cache and the memory is connect to the APB Interface of the Cortex M0. This results is multiple cycles of delay for each read and write operation we perform in which the processor stalls completely. The first cycle we loose is the AHB to APB bridge, then each DRAM access internally needs ~9 cycles at 300MHz to fetch or write the data, which translates to ~2 additional CPU cycles at 50MHz and finally another APB to AHB cycle. So in total we have at least 4 cycles of delay for each read or write operation. This also accounts for instructions, which inflicts a huge performance penalty, even if we only work on registers in the uC.
Drawing 1: System architecture without cache

To improve performance we add a Cache that is connected to the AHB interface and the memory controller. This reduces the number of stall cycles and thus increases the overall performance.
## Structure
In the next Chapter, some basics concerning the used technology will be explained. Chapter 3 is giving a brief introduction to caching strategies and technologies. Chapter 4 presents the created design and chapter 5 gives some final remarks.
# Basics
## ARM Cortex M0
The ARM Cortex M0 is the smallest available ARM Cortex model. It is classified as a 32bit RISC microcontroller with a 3-stage pipeline. To keep this pipeline filled, the Cortex M0 has an instruction buffer for two instruction, plus two instructions that can be fetched at once. This means the next four instructions are always available.
Since we have an estimate delay of four cycles for each load, the buffer and instructions on the fly can barely suffice the processors needs for an instruction to at each cycle. Additionally the instruction loads are competing with the data loads for memory access. And since data and instructions are usually in separate parts of the memory, additional latency occurs due to possible bank switching in the DRAM memory. <SOURCE>
## AHB-Lite
The AHB-Lite stands for “Advanced Highperformance Bus” and is a protocol and interface that is used on the ARM AMBA bus-system to provide high-bandwidth operations for the participators.It is a Master/Slave split phase transaction bus-system, where the master request reads/writes from/to slaves, that is implemented as a memory mapped interface. The two phases are address phase and data phase, which overlap each others. This means that during the data phase, the next address is already written to HADDR, so that the next cycle can begin as soon as the old ome is completed.

Drawing 2: AHB-Lite Architecture
- Address Phase: The master writes the desired address to HADDR. The decoder snoops it and notifies the responsible slave with the HSEL signal. Data phase begins as soon as the Master signals HREADY.
- Data Phase: The Slave is then reading/writing the data. If the action that needs to be performed takes longer than one bus cycle, the slave signals this with the HREADYOUT signal. It can extend the data phase until it can deliver the data or secured the read. The slaves writes to HRDATA, which is multiplexed back to the master.
Actually, there is number of additional signals and interactions that can occur during a bus transaction, but for the understanding of the project, the given description is sufficient. For more information see UG388.
## Memory Controller

Drawing 3: AHB-Lite read transfer. Notice that the address for transfer B is already put on the bus, while transfer A is still in the data phase.
To access the DRAM the standart Xilinx memory controller IP is used. It has a six channels to which devices can connect. Each channel is divided into a command path, a read path and a write path. Two channels are bidrectional, four channels are unidirectional. To access the DRAM, one bidirectional channel is used. This channel uses the same clock as the cache controller itself.
The memory in this project is a 16 Mbyte DDR2 memory that operates at ~300MHz.
## Performance Indicators
Since the project aims to improve the memory throughput most significant performance indicators are the memory access latency and the available read and read/write bandwidth. These metrics can be used to benchmark applications that are heavily bound to memory operations. However, operations the are calculation bound, we still can achieve a speedup by reducing the instruction fetch latency.
However, they can only be used to indicate the overall application performance development and tells us nothing about the cache controller. To check how well out cache is actually performing, the most important metric would be the hitrate. It is the percentage of memory reads that actually result in a successful cache lookup. The higher this number is, the better.
# Cache
There is a huge demand on large amounts of high speed memory. High speed memory is cost-intensive and of small size commonly less than 1 MB, high density memory with large capacity is cheap and slow. An economical way to satisfy this demand is to use memory hierarchies, which takes advantage of locality and trade-offs in the cost-performance of memory-technologies.

The principle of locality, says that most programs do not access all code or data uniformly. Locality occurs in time (temporal locality) or in space (spatial locality). This principle led to hierarchies based on memories of different speeds and size.

Since fast memory is expensive, a memory is organized into several levels, each smaller, faster and more expensive per byte than the next lower level, which is further away from the CPU. The hierarchy is in most cases transparent to the CPU and moreover to the programmer, which means that there is a virtual memory address space to the CPU and the data is physically stored somewhere in the memory hierarchy (comp. Computer-Architecture-A-Quantitative-Approach-5th edition, Page 72 – 73).

The memory is usually organised in words, each of the size of multiple bytes e.g. 2, 4, 8, 16 or more bytes and a group of words are called a block or a line with e.g. 2, 4, 8, 16 or more words.

When a word is not found in the cache, the word must be fetched from a lower level memory and placed in the cache before continuing. For efficiency reasons more than one word, the so called cache line is moved in the cache, because it is likely that they are needed soon due to the spatial locality. Each cache line includes a tag to indicate which memory address it represents.

The cache storage scheme defines where a cache line can be placed in the cache. The set associative scheme separates the cache into multiple sets. A set is a group of cache lines. A cache line is first mapped onto a set and then the cache line can be placed anywhere within that set. Finding a cache line consists of first mapping the cache line address to the set and then search the set – usually in parallel – to find the cache line. The set is usually chosen by the address of the data, by way of modulo operation.

If there are n cache lines in a set, the cache placement is called n-way associative. The end points of set associativity have there own names. A direct-mapped cache has just one cache line per set i.e. a cache line is always placed in the same location and a fully associative cache has just one set i.e. a cache line can be placed anywhere (comp. Computer-Architecture-A-Quantitative-Approach-5th edition, Page 74).

When data in a cache line is modified the main memory needs to be updated somehow. There are two major strategies to handle the consistence of the main memory. The write-through cache updates the item in the cache and writes through to update the main memory. A write-back cache only updates the cache and when the cache line is about to be replaced, the cache line is copied back to the main memory. Both write strategies can use a write buffer to allow the cache to proceed as soon the data are placed in the buffer rather then wait until the write to main memory completes.

If there is more than one entity able to write to the main memory it is necessary to take care of the consistence of the cache in relation to the main memory. For this purpose a cache line further comprises a dirty flag, which indicates that the representative of that cache line in the main memory has changed. If the CPU wants to read the data and would normally get a cache hit, would in this case get a cache miss because of the dirty flag and has to wait for a normal read cycle from the main memory to proceed.
# Implementation
## Performance without Cache
Since the uC has no data cache, an the instrcution cache is to small to hold a significant number of instructions, the performance is expected to be very low. We measured the bandwidth that we can achieve with the current setup and and the results are displayed in the table below.
Benchmark	Bandwidth (Kbyte/s)
Global Sum (Read only Access)	2
Prefix Sum (Read and Write Access)	1

We used two benchmarks to determine the performance. A global sum, which only requires a subsequent number of reads, and a prefix sum that consists of two reads and one write. Since one of the reads is the previous value, we can assume that it remains in a register for use in the next calculation. So we have one read and one write. This is also displayed in the benchmark results, where the global sum has two times the bandwidth, compared to the prefix sum where reads and writes compete for memory access. Both benchmarks perform a single addition operation.
Both benchmarks have been performed with 32bit interger values, to eliminate delays due to floating point arithmetics. Since we have no caches, or other resources that can alter the performance over diffferent problem sizes, the benchmark results are consistent over all (reasonable) problem sizes.
## Cache implementation
For this project we decided to use a direct mapped cache. This type of cache is straightforward to implement and can deliver data with the least latency, because there is no need to a hit-compare between the sets.
To cache the 16Mbyte of memory, we will create a unified cache with the size of 4kByte, divided into cache lines with the size of 32 bytes. This means 128 cache lines that can, for example, hold 8 32bit values or 16 16bit instructions. The cache is byte adressanble. The cache is designed with as write-through. This means that a write is always relayed to the DRAM, while the cache line is updated. We use one bit to Invalidate a cache line. The invalidate has to requested by the processor, since we potentially have other devices accessing the memory, like the DMA . The invalid bit is stored along the tag.
A downside of this method is possible thrashing of data, when instructions and data reside in different areas of the memory, that map to the same cache line. However, since we are on an embedded system, we can avoid that by manually placing the data in a memory area that is not affected by this (granted, the data is small enough).
We aim to run the cache controller at 100MHz clock-synchronous with the 50MHz AHB-Lite bus. In case of a read access, this gives us two bus cycles to dertermine a cache-hit and deliver the data to the bus. This would result in a zero cycle hit response. A cache miss results is an extended data phase, since the data needs to be fetched from the DRAM. A write requst can almost always be serviced in a single cycle. A more detailed behavioiral analysys is given in the section describing the state-machines.
The controlling logic of the cache consists of two state-machines, one for reading and one for writing, that run indenpended from one another.
The actual memory is generated out the available SRAM blocks on the fabric. We use two dual port SRAM blocks with a size of 18Kbit, one for tags and one for the data. This allows parallel access to both memories from both state-machines, if necessary.
### Read Statemachine
Designing the read state-machine was one of the biggest challenges during the implementation, since a lot of coner cases, especially after a cache miss, need to be considered.
To reduce the cache-miss latency, the first word that is fetched from the DRAM is the requested word, no matter where in the cache line it is. The used memory controller however, does not support out-of-order bursts. In a worst case scenario we need three read-cycles on the DRAM to fetch all the data. First we need to read the requeste word, then we read up to the end of cache-line and then from the beginning till the requested word.
Since we the memory controller interface is only 32 bits wide, we need at least eight read cycles to fetch a full cache-line. Since the DRAM can be accessed by multi devices, we have no guarantee on how long it will take for a data-word to arrive in the read FIFO. This means that we have to poll the pX_rd_empty (de) signal to check if a new set of data has arrived.

Drawing 4: Statemachine for read access to DRAM
### Write Statemachine

Drawing 5: write statemachine
The write state-machine consits of three states, IDLE, TAG and WAIT. Usually the write state-machine simply forwards the data to the memory controller and updates the corresponding cache-line, if it is residing in the cache and is valid. In this case, the state machine transitions form IDLE to TAG and back as soon as the request is done. If there are subsequent requests, the state-machine resides in the TAG state as long requests keep incoming. If the memory controllers write-queue is full, the state-machine transitions into the WAIT state and stalls the bus until further requests can be handled. Since the AHB-Lite bus has overlapping data and address phases we need two stages of registers to save the address until we get the data from the bus. This covers the worst-case scenario of many subsequent writes to different banks of the DRAM.
### Integration
## Performance with Cache
# Concluding Remarks